## Slide 1: Fingerprint Solution R&D
Pilot Deployment

## Slide 2: Commercial Solution Challenges
Cost of large-scale commercial solutions
Security concerns due to proprietary solution
Integration to our existing systems
Cannot be customized further

## Slide 3: In-House Solution Challenges
Significant processing in matching fingerprint vs number
Most fingerprint tools (SDK) advertise 10K/sec matching speed
Unacceptable delay when 50K or more
Skills and knowledge required
Development time required

## Slide 4: Sequential Fingerprint Matching
1 FP
10K FP
1M FP
1 sec
100K FP
10 sec
100 sec
Sequential Matching

## Slide 5: Benchmark Results for Sequential Matching
Processor Type | Fingerprints | Seek Time
3rd Gen Intel Core i5-2430M | 17K | 1 sec
Dual Core @ 2.4GHz | 1M | 58 sec
 | 10M | 588 sec (9.8 min)
2x Quad-Core Intel Xeon E5450 | 12.5K | 1 sec
2x4 Cores @ 3.0GHz | 1M | 80 sec (1.3 min)
 | 10M | 800 sec (13 min)

## Slide 6: The Research Project

## Slide 7: Sequential vs Multithreaded
1 FP
10K FP
1M FP
1 sec
100K FP
10 sec
100 sec
Sequential Matching
1 FP
10K FP
1M FP
1 sec
100K FP
Multithreaded Matching
1 sec
1 sec
1 core
1 core
1 core
1 core
1 core
1 core
1 core
1 core

## Slide 8: Multithreaded Benchmark Results
Processor Type | Fingerprints | Seek Time | CPU Core
3rd Gen Intel Core i5-2430M | 17K | 1 sec | 1 Core
Dual Core @ 2.4GHz | 1M | 1 sec | 58 Cores
 | 10M | 1 sec | 588 Cores
2x Quad-Core Intel Xeon E5450 | 12.5K | 1 sec | 1 Core
2x4 Cores @ 3.0GHz | 1M | 1 sec | 80 Cores
 | 10M | 1 sec | 800 Cores

## Slide 9: Solution Diagram
1 sec response time
< 1 sec response time
< 1 sec response time

## Slide 10: Speed Optimization and Cost Reduction Measures
Multi-core and multithreaded matching
In-app memory cache in server cluster
Search priority based on location with in-premise cache
Search priority based on frequency of attendance
Real-time cache reduction algorithm
Server clustering and utilization of existing servers
Option of renting commercial cloud servers
Notes: In-App memory cache of the whole FP dataset (minutia) for high-speed matching in the primary data center
Multi-core and multithreaded matching algorithm for max utilize hardware utilization and max speed due to multiple concurrent matching operations
Speed optimization algorithm that prioritized searches based on expected attendees' geographical location (search origin and location code)
Speed optimization algorithm that prioritized searches based on attendance history and customer’s frequency of attendance
Extra layer of in-premise in-app memory cache in the main and satellite location level to reduce data needed to reach the global data center
Real-time Cache Reduction Algorithm after authentication and verification to lessen the max number of requests when searching
Fingerprint Node Clustering and utilization of our other existing server's processing power when more processing power is needed
Option of renting commercial cloud computing capacity to reduce our cost by not purchasing all the necessary server hardware jus for searching larger records like 10-100M of FP but won't be utilized after attendance hours.

## Slide 11: Solution Summary & Benefits
In-house software and hardware solution
We hold the source code, we control the security
Integrates well with our existing systems and processes
We can utilize our existing hardware to maximize cost savings
Can be extended and improved when the need arises
Notes: Custom designed software and hardware solution
Utilizes our existing infrastructure and assets to maximum cost savings and speed
Integrates well with our existing process and system
We hold the source code
Fully optimized to our org's culture and process and to take advantage of the knowledge we have which external vendors don't have to provide the best experience and best security for our customers

## Slide 12: Cost Factors
Fingerprint Scanners ($50 to $75 each)
Fingerprint Matching Server (64 to 128-core)
Workstations for the main and satellite locations (regular PCs or touchscreens)
Fingerprint SDK Licenses (matching utility)
  Paid Option – Griaule SDK @ $5,500 USD per 150 PCs
  Open source – Free (needs to be tested)
Other software licenses
Premises construction expenses
Deployment timeline

## Slide 13: Cost Estimates
Estimates for data center and main location (1M Fingerprints for 1 sec):
Fingerprint Scanners = 25 x $75 = $1,875
Server Cluster Hardware 64-Core = $2,500 1U Server X7DCA-L 2x Xeon L5420 2.5ghz Quad Core x 8 @ $200
Workstations for fingerprint device = 10 x $500 = $5,000
Misc. expenses = $5,000
Licenses -
-------------
TOTAL: $14,375 USD
Estimate per satellite location deployment:
Fingerprint Scanners = 2 x $75 = $150
Touchscreen Workstation (Kiosk) = 1 x $700 = $700
Internet Access -
-------------
TOTA: $850 USD

## Slide 14: Research Summary
Completed research areas:
System architecture design
Linear matching speed (10K – 17K/sec)
Multicore matching speed (up to 8-core, ~100K/sec)
Single-node server cluster (local-internet-local)
Pending research areas:
End-to-end single-user testing
End-to-end simultaneous users (10+)
Multiple clustered servers testing (if needed)
Long-term system stability and overall user experience
Detailed costing
Preliminary conclusion:
Low cost over commercial solutions
More advantages over commercial solutions
Research is very positive and implementation looks very feasible